## Slide 1
LED & TP
control block
FPGA Block Diagram 1 / 3
FPGA block diagram : both PS and PL side
Zynq XC7Z020
ADC3660
SEN
SCLK
SDIO
DCLK
FCLK
DA5/6
DB5/6
CLKP
CLKN
RESET
PDN
DCLKIN
PS_CLK
50MHz
10MHz
5MHz
ARM PLL
40MHz
ADC clock
control
block
ADC data
Rx block
x64
x1
40MHz
5MHz
ADC data
mixing & gain correction
block
x1
x64
DDR3
MT41K256M16
(16-bit, 256M)
Peak
detect
block
PS side
PL side
Ethernet PHY
(RTL8211)
LAN
(10/100)
CLK125M
GMII
MDIO
Analog
PD
signal
50MHz
CLKP/N
LPF
reference
voltage
1
FCLK1(160M)
temperature sensor (4ea)
- laser temperature
- env. temperature
DDR PLL
IO PLL
1000M
800M
ADC control block (SPI)
x64
Serial Flash
S25FL128
(16MB)
QSPI
UART
1000M
LED2 : MCU run (1 Hz)
LED4 : FPGA run (1 Hz)
LED3 : reserved
EEPROM
LED5 : reserved
Test Pin (TP8~TP11)
Protocol comm.
- TCP service (port 23)
- CMD Rx service
- EVT Tx service
Maintenance comm.
- TCP(7023) & UART
- monitoring service
- user CMD service
LAN link service
(10/100)
Miscellaneous feature
- Watchdog service
- fake PHD data gen.
- LED control
Laser control
- Laser on/off control
- Laser temp. control
fake ADC
data gen. block
Control REG
block
EEPROM control
block (SPI)
DMA + control block
(raw ADC write)
vtg to ch mapping table
(log scale, 512ch)
XADC (12-bit)
Vp/Vn Vad0~3
DPRAM +
particle counting
block
(512 ch)
vtg to ch determine
block
TCF calc.
block
ch A
ch B
GCF calc.
block
fake PHD
data gen.
block
HW component
color notification
FPGA F/W design finished
FPGA circuit design finished
FPGA circuit to be designed
temp. PID
control block
DAC
ADC data
single capture

## Slide 2
Acronyms
- GCF : Gain Correction Factor
- TCF : Turbidity Correction Factor
Analog
PD signal
x64
x1
ADC
3660
RXD_B
Select : 12.5 mV boundary
ADC_x1 ≥ 0x100 : Z = RXD_B
ADC_X1 < 0x100 : Z = RXD_A
PS : BASE_REF
- 750 mV (0xC000)
MULT
MUX
MULT
64
A
B
Z
MULT
Ch A
Ch B
ADC_RXD[31:0]
ADC_DONE
XADC
(FPGA)
LPF
PS : BASE_MEAS
R6 : TCF
(Turbidity Correction Factor)
(Q2.14 format)
=
R5 : X64_GCF
(Gain Correction Factor)
(Q2.14 format)
=
Constant
value
Register
(PS calculate)
Register
(PS setting)
R1 : NOISE_TH
R2 : PLS_WIDTH_MIN
R3 : PLS_WIDTH_MAX
R4 : PLS_INTV_MIN
R0 : CTRL_REG
PS measure
Note : XADC res =
FPGA Block Diagram 2 / 3
FPGA block diagram : ADC data manipulation detail
MUX
0x4000
= 1.0000(Q2.14)
GCF_EN
MUX
0x4000
= 1.0000(Q2.14)
TCF_EN
RXD_A[15:0]
RXD_B[15:0]
Neg.
cancel
&
Pos.
range
shift
EN
EN
output : offset binary
ADC_MIXER
Baseline
Wander
Tracking
&
Corrector
ADC_
RXD
DC
Offset
Correct
RXD_A

## Slide 3
FPGA Block Diagram 3 / 3
Baseline wander tracking & rejection basic idea
- 2 methods considered, choose method 2
- LPF(Low Pass Filter) : implemented using FIR(Finite Impulse Response) Filter
HPF
(High Pass Filter)
Delay
+
-
Moving Average
Filter
Delay
+
-
LPF
(Low Pass Filter)
+
-
Delay
Method 1) using High Pass Filter & Moving Average Filter
① input signal
Method 2) using Low Pass Filter
③ filtered signal = ① - ②
② Filter output
① input signal
② Filter output
③ filtered signal = ① - ②

## Slide 4
FPGA Block Diagram 4 / 3
FIR (Finite Impulse Response) Filter : 공식은 아래식과 같으며 구성은 2가지 방법 중 선택하여 구현
Y[n] = C0·X[n] + C1·X[n-1] + C2·X[n-2] + C3·X[n-3] + · · · · · + Cn·X[n-M]
M = number of tap, Cn = filter coefficient, X[n] = input, Y[n] = filtered output
filter tap 및 filter coefficient 는 filter 특성 simulation 하면서 결정 필요.
multiplier
register(delayed data)
adder
- multiplier operates simultaneously
- addition requires stepped delay, because all additions can not be operated at the same time
Direct form FIR filter
Transposed form FIR filter
Baseline wander tracking & rejection detail

## Slide 5
FPGA Block Diagram 5 / 3
- 필요 resource(multiplier, adder) 사용 최소화 위해, serial 및 parallel 동작 mix 된 형태로 구성
- Filter 특성 :
1) band width 5%, 75dB attenuation (-75dB = 0.00018)
2) FIR Filter Tap = atten / 22 x Fs / (Fstop – Fpass) = 75 / 22 x 100 / 5 = 69 taps
3) Filtered output, Y[n] = C0·X[n] + C1·X[n-1] + C2·X[n-2] + · · · · · + C68·X[n-68] // 69 taps
= YS[fir_0] + YS[fir_1] + YS[fir_2] + · · · · · + YS[fir_13] // 14 parallel FIR x 5 serial FIR
4) serial FIR, YS[n] = C0·X[n] + C1·X[n-1] + C2·X[n-2] + C3·X[n-3] + C4·X[n-4]
Serial-parallel FIR filter
Serial FIR_0
(for tap : 0~4)
Serial FIR_1
(for tap : 5~9)
Serial FIR_13
(for tap : 65~69)
Serial FIR_2
(for tap : 10~14)
X[n]
C[68:0]
X[n-4]
X[n-9]
X[n-14]
X[n-64]
YS[0]
YS[1]
YS[2]
YS[13]
Y[n]

## Slide 6
FPGA Block Diagram 6 / 3
- FIR filter 1 단으로 구성시 38,000 개의 tap 이 필요함. (= 38,000 개의 multiplier + adder 필요)
- 69 tap 사용한 FIR filter 3 단 cascading 형태로 구성.
- down sampling 시 alias 문제 해결을 위해 LPF 가 필요함.
FIR filter cascading
LPF
LPF
LPF
X[n]
Y[n]
< FIR Filter 1 >
- Fs : 10 MHz
- Fc : 150 KHz
- Fstop : 300 KHz
down sampling
1/16 = 625KHz
< FIR Filter 2 >
- Fs : 625 KHz
- Fc : 15 KHz
- Fstop : 30 KHz
< FIR Filter 3 >
- Fs : 39 KHz
- Fc : 2 KHz
- Fstop : 4 KHz
down sampling
1/16 = 39KHz

## Slide 7
FPGA Block Diagram 7 / 3
Baseline wandering 제거용 Filter 특성 결정을 위한 analog 신호 주파수 성분 추정
- analog 신호 주파수 범위는 10 KHz ~ 50 KHz 정도로 추정
- 여유를 더해 Filter Fc(cutoff 주파수) 는 1 KHz 로 선정
10 usec
(50 KHz)
100 sample
20 usec
(25 KHz)
200 sample
50 usec
(10 KHz)
500 sample
sampling : 10 MHz (100 nsec)

## Slide 8
FPGA Block Diagram 8 / 3
ADC_X1
(16-bit)
ADC_X64
(16-bit)
PD raw
ADC signal
MSB
ADC_MIXED
(32-bit)
LSB
ADC
signal
Mixer
ADC_X1
ADC_X64
ADC_MIXED
DMA_addr + 0
DMA_addr + 1
DMA_addr + 2
DMA_addr + 3
DMA_addr + 4
DMA_addr + 5
DMA_addr + 6
DMA_addr + 7
DMA_addr + 8
DMA_addr + 9
DMA_addr + 10
DMA_addr + 11
DMA_addr + 12
DMA_addr + 13
DMA_addr + 14
DMA_addr + 15
DMA_addr + (N-1) x 8 + 0
DMA_addr + (N-1) x 8 + 1
DMA_addr + (N-1) x 8 + 2
DMA_addr + (N-1) x 8 + 3
DMA_addr + (N-1) x 8 + 4
DMA_addr + (N-1) x 8 + 5
DMA_addr + (N-1) x 8 + 6
DMA_addr + (N-1) x 8 + 7
. . . . .
1st ADC data
2nd ADC data
Nth ADC data
FPGA block diagram : ADC data DMA data allocation

## Slide 9
FPGA Block Diagram 9 / 3
base line : 400 mVdc
signal : 0 mV
Case 1)
PD
Simulator
Analog Circuit DC offset voltage measure
H-sensor
GND
Case 2)
PD
Simulator
H-sensor
GND